Geant4 Evaluation and Optimization of Portable Faraday Cup

---
Overview
Evaluation (% charge defect [%cd])
HIT, Geant4
Optimization
MCNP6: Height, Radius
Geant4: film thickness, %cd minimization
Validation
G4 Energy Spectra, go99 branching ratios
Discussion
Dosimetric quiver plot, Deposition Histogram

---
Evaluation
Charge defect = ([q_in – q_out] – q_beam)/q_beam
Assumption:
Deposition/Removal of charge in Kapton produces mirror charge in Copper with magnitude linearly proportional to depth in Kapton between Copper and Silver interfaces

---
Evaluation
Fig 1: Comparison of Geant4 and HIT Experimental charge defect measurements

---
Optimization
Fig 2: Charge defect measurement for coarse device dimension optimization

---
Optimization
Goal: Minimize |%cd| by fine-tuning dimensions
Thus:
Obtain functional Kapton thickness of energy
such that [%cd](E=X, t_KA=Y) = 0
Preliminary results show Y=36 microns when X=160 MeV

---
Validation
Fig 3: a) Beta spectra and b) gamma spectra in Copper via Geant4

---
Discussion
Fig 4: Energy deposition gradient for electrons via Geant4; note both spray and halo/aura presence

---
Discussion
Fig 5: Proton deposition count in Copper via Geant4

---
Discussion
Fig 5: Neutron deposition count in Copper via Geant4